# tiny编译器使用
计算阶乘tiny源码：
{ Sample program in TINY language - computes factorial } read x; { input an integer } if 0 < x then { don't compute if x <= 0 } fact := 1; repeat fact := fact * x; x := x - 1 until x = 0; write fact { output factorial of x } end

编译生成的目标代码:
0: LD 6,0(0) 1: ST 0,0(0) 2: IN 0,0,0 3: ST 0,0(5) 4: LDC 0,0(0) 5: ST 0,0(6) 6: LD 0,0(5) 7: LD 1,0(6) 8: SUB 0,1,0 9: JLT 0,2(7) 10: LDC 0,0(0) 11: LDA 7,1(7) 12: LDC 0,1(0) 14: LDC 0,1(0) 15: ST 0,1(5) 16: LD 0,1(5) 17: ST 0,0(6) 18: LD 0,0(5) 19: LD 1,0(6) 20: MUL 0,1,0 21: ST 0,1(5) 22: LD 0,0(5) 23: ST 0,0(6) 24: LDC 0,1(0) 25: LD 1,0(6) 26: SUB 0,1,0 27: ST 0,0(5) 28: LD 0,0(5) 29: ST 0,0(6) 30: LDC 0,0(0) 31: LD 1,0(6) 32: SUB 0,1,0 33: JEQ 0,2(7) 34: LDC 0,0(0) 35: LDA 7,1(7) 36: LDC 0,1(0) 37: JEQ 0,-22(7) 38: LD 0,1(5) 39: OUT 0,0,0 13: JEQ 0,27(7) 40: LDA 7,0(7) 41: HALT 0,0,0

执行：
$ tm SAMPLE.tm TM simulation (enter h for help)... Enter command: h Commands are: s(tep <n> Execute n (default 1) TM instructions g(o Execute TM instructions until HALT r(egs Print the contents of the registers i(Mem <b <n>> Print n iMem locations starting at b d(Mem <b <n>> Print n dMem locations starting at b t(race Toggle instruction trace p(rint Toggle print of total instructions executed ('go' only) c(lear Reset simulator for new execution of program h(elp Cause this list of commands to be printed q(uit Terminate the simulation Enter command: g Enter value for IN instruction: 5 OUT instruction prints: 120 HALT: 0,0,0 Halted Enter command:

可以看到输出结果：OUT instruction prints: 120
寄存器值：
Enter command: r 0: 120 1: 0 2: 0 3: 0 4: 0 5: 0 6: 1023 7: 42